## Slide 1: Urban land-use mapping using a deep convolutional neural network with high spatial resolution multispectral remote sensing imagery
Deteção Remota Multiespectral Sílvia Mourão fc57541
FCUL, 17/05/2022

## Slide 2: Index
Introduction
Area of Study
Methodology
Results

## Slide 3: Introduction
Objective: creating an urban land-use map from high spatial resolution multispectral remote sensing images
Problems
  High spatial resolution images are very complex
  Methods are very dependent on the classification system
  They require previously acquired information about the terrain
  The images need to be divided into small uniform processing units
Classic Techniques
  Pixel Classification
  Object Classification
  Graph-Based Classification

## Slide 4
Deep Learning – Convolutional Neural Network is a possible solution that obtains good results
Introduction
Two proposed solutions: transfer learning and small DCNN - not directly applicable to HSR images
Problem: for HSR images it requires a high number of layers which translates into an elevated number of training samples
Proposed use of a skeleton based decomposition method instead of uniform processing units
Creation of a new method: STDCNN – combines both solutions

## Slide 5: Area of Study
Hong Kong
WorldView-3
1.24m
8 channels
Shenzhen
WorldView-2
0.5 m
4 channels

## Slide 6
Area of Study
The authors considered 11 different classes for training

## Slide 7
Area of Study
Hong Kong = 36 training samples, 15-25 testing samples
Shenzhen = 40 training samples, 30 testing samples
Dimension 256 x 256 px

## Slide 8
Creation of STDCNN:
Transferred DCNN uses AlexNet trained set – allows the STDCNN to gain a deep architecture
Small DCNN with reduced level of convolution and pooling layers – can work with multispectral images
Two final layers - fully connected and softmax – join the results of the two paths
Methodology

## Slide 9
Decomposing the image with the skeleton based method
For each area of the skeleton all processing units belonging to that area are used
Results are combined to generate the land-use map
Methodology

## Slide 10
STDCNN proposed method was tested versus other methods previously proposed by other authors
Confusion Matrices created for each case
Two indicators considered – Overall Accuracy (OA) and Kappa Coefficient
Results

## Slide 11
Land-use maps created with skeleton-based decomposition and uniform decomposition methods
Skeleton-based decomposition obtained better, smoother results
Results

## Slide 13
Huang, B.; Zhao, B.; Song, Y. Urban Land-Use Mapping Using a Deep Convolutional Neural Network with High Spatial Resolution Multispectral Remote Sensing Imagery. Remote Sensing of Environment 2018, 214, 73–86. https://doi.org/10.1016/j.rse.2018.04.050